## Slide 1: Conclusion
RQ1
Can a model be lifted to a higher level of theory by relabelling only a subset of its training data?
Yes, as long as the spin formalism is not changed with the labels
• Under 1 % relabelled: force error to a third in every tier, energies improve in every tier, geometries as good as MACE's
• Barriers: error drops to a third at low MR; at mid and high MR the correction overshoots, mostly the base model's error
• The correction is bounded by the base model: 42 meV of MACE's own error pass through unchanged
RQ2
Can a model learn a surface from paths that were never relaxed on that surface?
Yes when only the level of theory changes. No when the spin formalism changes as well
• At broken-symmetry transition states the models deliver structures that are not stationary points: DFT residual forces 2.5 times larger, while their own forces report convergence
• Force error two to three times larger, energies within chemical accuracy: the barrier error is a geometry error
• Part of this is multireference character itself; at equal MR character a factor of about 1.6 remains
• Two candidate causes: the training data, never relaxed on the unrestricted surface, and the shape of that surface. The data do not decide

## Slide 2: Implications and outlook
A test that needs no reference. One unrestricted DFT single point with a stability analysis at the structure a model delivers. It shows for any model and any reaction whether a stationary point of the unrestricted surface was found
In practice. Run it at every transition state that is trusted further: as a training point, a reference or a starting point
Benchmarks. None tests models at broken-symmetry transition states; reported success rates were measured on restricted references
Future work. Fine-tune on paths relaxed on the unrestricted surface. If the training data are the cause the errors disappear; if the shape of the surface is the cause they remain. The same paths give a benchmark of broken-symmetry saddles